## Slide 1: Key Input & Interrupt
2026.01.19

## Slide 2: Key Button
PF9 – SW1 KEY1에 할당
PF10 – SW2 KEY2에 할당

## Slide 3: Key Button
PF9, GPIO_Input 설정 후 – KEY1으로 이름 변경
PF10, GPIO_Input 설정 후 – KEY2로 이름 변경
두 핀 모두 Pull-up으로 설정한다.

## Slide 4: No Interrupt Key Test
void KEY_Test(void) {
HAL_GPIO_WritePin(GPIOF, LED1_Pin|LED2_Pin|LED3_Pin, GPIO_PIN_SET);
while(1) {
if(HAL_GPIO_ReadPin(KEY1_GPIO_Port, KEY1_Pin) == GPIO_PIN_RESET) {
HAL_GPIO_WritePin(LED1_GPIO_Port, LED1_Pin, GPIO_PIN_RESET);
} else {
HAL_GPIO_WritePin(LED1_GPIO_Port, LED1_Pin, GPIO_PIN_SET);
}
/* Key가 눌리면 GPIO 값이 Low가 된다 */
if(HAL_GPIO_ReadPin(KEY2_GPIO_Port, KEY2_Pin) == GPIO_PIN_RESET) {
HAL_GPIO_WritePin(LED2_GPIO_Port, LED2_Pin, GPIO_PIN_RESET);
} else {
HAL_GPIO_WritePin(LED2_GPIO_Port, LED2_Pin, GPIO_PIN_SET);
}
}
}

## Slide 5: No Interrupt Key Test
처음에 모든 LED Off
Key1을 누르면 LED1 On
Key2을 누르면 LED2 On

## Slide 6: Exception 종류
위치 | Exception type | Priority | 설명
0 | - | - | 리셋 시 vector table의 첫 entry
1 | Reset | –3 (highest) | Power up과 Warm reset시.
2 | Non-maskable Interrupt (NMI) | -2 | pre-empted되지 않는다.
3 | Hard Fault | -1 | 모든 종류의 Fault
4 | Memory Management | Configurable | MPU mismatch
5 | Bus Fault | Configurable | Pre-fetch, memory fault
6 | Usage Fault | Configurable | Undefined instruction
7~10 | - | - | Reserved
11 | SVCall | Configurable | System service 호출
12 | Debug Monitor | Configurable | not halting Debug monitor
13 | - | - | Reserved
14 | PendSV | Configurable | Pendable request
15 | SysTick | Configurable | System tick timer.
16~ 255 | External Interrupt | Configurable | core 밖 외부 interrupt (0~239)

## Slide 7: pre-emption 상태 stack 변화
interrupt 발생시 CPU는 자동으로 processor의 상태를 exception의 stack에 저장하고 빠져 나올 때 Interrupt Service Routine (ISR)의 끝에서 복구를 시켜준다.
여기에 저장되는 레지스터들은 R0-3, R12, LR, PSR, PC 등이다.
자동 처리로 인해서 general한 C 함수를 interrupt handler로 쉽게 사용할수 있고, IRQ 지연 시간도 줄어든다. (특별한 어셈블리 분기 stub을 만들 필요가 적고, C로 정의한 함수 심볼 주소를 그대로 사용하기 편하다)
pre-emption이 일어난 상태에서의 stack의 변화 모양은 위 그림. xPSR부터 시작해서 8개의 레지스터가 차례로 저장되어 있는 모습

## Slide 8: STM32 Vector table

## Slide 9: EXTI 설정

## Slide 10: EXTI 설정
NVIC interrupts enable

## Slide 11: EXTI 설정
NVIC interrupts code generation

## Slide 12: External interrupt GPIO mapping

## Slide 13: External interrupt

## Slide 14: External interrupt/event controller block diagram

## Slide 15: NVIC_Configuration
#define KEY1_EXTI_IRQn EXTI9_5_IRQn
#define KEY2_EXTI_IRQn EXTI15_10_IRQn
static void MX_GPIO_Init(void) {
… … … … … …
/*Configure GPIO pins : KEY1_Pin KEY2_Pin */
GPIO_InitStruct.Pin = KEY1_Pin|KEY2_Pin;
GPIO_InitStruct.Mode = GPIO_MODE_IT_FALLING;
GPIO_InitStruct.Pull = GPIO_PULLUP;
HAL_GPIO_Init(GPIOF, &GPIO_InitStruct);
…
}
static void MX_NVIC_Init(void) {
/* EXTI9_5_IRQn interrupt configuration */
HAL_NVIC_SetPriority(EXTI9_5_IRQn, 0, 0);
HAL_NVIC_EnableIRQ(EXTI9_5_IRQn);
/* EXTI15_10_IRQn interrupt configuration */
HAL_NVIC_SetPriority(EXTI15_10_IRQn, 0, 0);
HAL_NVIC_EnableIRQ(EXTI15_10_IRQn);
}

## Slide 16: EXTI IRQHandler
void EXTI9_5_IRQHandler(void)
{
HAL_GPIO_TogglePin(LED1_GPIO_Port, LED1_Pin);
HAL_GPIO_EXTI_IRQHandler(KEY1_Pin);
}
void EXTI15_10_IRQHandler(void)
{
HAL_GPIO_TogglePin(LED2_GPIO_Port, LED2_Pin);
HAL_GPIO_EXTI_IRQHandler(KEY2_Pin);
}

## Slide 17: Interrupt Key Test
처음에 모든 LED On
화면에 계속 문자열 출력
Key1을 누르면 LED1 Toggle
Key2을 누르면 LED2 Toggle