## Slide 1: UART1 테스트
CRZ Technology

## Slide 2: Mango-M32F2 UART1 테스트

## Slide 3: STM32CubeIDE 프로젝트 생성
STM32CubeIDE 실행.

## Slide 4: STM32CubeIDE 프로젝트 생성
workspace 설정

## Slide 5: STM32CubeIDE 프로젝트 생성

## Slide 6: STM32CubeIDE 프로젝트 생성
“File” 클릭, “New” 클릭, “STM32 Project” 클릭.

## Slide 7: STM32CubeIDE 프로젝트 생성
“STM32F207VGT6“ 선택 후 "Next” 클릭

## Slide 8: STM32CubeIDE 프로젝트 생성
Project Name으로 “uart1_prj” 입력 후 “Finish” 클릭.

## Slide 9: Pinout view

## Slide 10: Clock / UART1 pinmap
25MHz external clock - PH0 / PH1
UART1 - PB6 / PB7

## Slide 11: Pinout view
PH0 – RCC_OSC_IN 선택

## Slide 12: Pinout view
PH1 – RCC_OSC_OUT 선택

## Slide 13: Pinout view
PB6 - USART1_TX, PB7 – USART1_RX 선택.

## Slide 14: RCC 설정
“System Core"에서 “RCC” 클릭.

## Slide 15: RCC 설정
“High Speed Clock(HSE)"에서 “Crystal/Ceramic Resonator”클릭

## Slide 16: Clock Configuration
“Clock Configuration“ 클릭 후 Clock Frequency 설정

## Slide 17: UART1 설정
“Connectivity“ 클릭, “USART1” 클릭.

## Slide 18: UART1 설정
“Mode“, “Asynchronous” 클릭.

## Slide 19: UART1 Test Project
“Save All“클릭, Code Generation.

## Slide 20: UART1 Test Project
core/src/main.c 편집
  printf() – UART1, overwrite _write() function
    /* Private user code ---------------------------------------------------------*/
    /* USER CODE BEGIN 0 */
    #define hUART huart1
    int _write( int32_t file , uint8_t *ptr , int32_t len )
    {
    /* Implement your write code here, this is used by puts and printf for example */
    for ( int16_t i = 0 ; i < len ; ++i )
    {
    HAL_UART_Transmit( &hUART, ptr++, 1, 100);
    }
    return len;
    }
    /* USER CODE END 0 */
    /* USER CODE BEGIN 2 */
    int count = 0;
    printf(“UART1 test\r\n");
    /* USER CODE END 2 */
  /* Infinite loop */
  /* USER CODE BEGIN WHILE */
  while (1)
  {
  printf("count=%d\r\n", count++);
  HAL_Delay(1000);
  /* USER CODE END WHILE */
  /* USER CODE BEGIN 3 */
  }
  /* USER CODE END 3 */

## Slide 21: Hex File Generation
“uart1_prj” 우클릭, “Properties“ 클릭.

## Slide 22: Hex File Generation
“C/C++ Build“-“Settings”-“Tool Settings“-“MCU Post build outputs“-“Convert to Intel Hex file (-O ihex) 클릭,
“Apply and Close” 클릭.

## Slide 23: Project Build
“Project”클릭, “Build All“ 클릭.

## Slide 24: Test 결과 확인
3핀 serial cable을 UART3에 연결하고 Flash Loader로 다운로드.
3핀 serial cable을 UART1에 연결하고 결과 확인.
RCC / Clock Configuration / UART1 설정은 나머지 실습에 공통.